## Slide 1: Welcome to MATLAB DigComm LAB
  Matlab Toutrial
    http://www.math.utah.edu/lab/ms/matlab/matlab.html#starting
  LAB1 to LAB5 : BASIC WAVES
  LECTURE: Complex Exponential Function
    LAB6 to LAB7
  Channel Modeling
    LAB8
  OFDM modeling and Error Rate Measure
    LAB9 to LAB11
  REPORT TASK

## Slide 2: LAB1： AM
Write Amplitude Modulation (AM) program by MATLAB
A = 1 + 0.5*cos(2*pi*1*t)
fc =5Hz
Use Sampling frequency fs = 100Hz

## Slide 3: LAB1： AM answer
n=0:1000; % 1001 points
fc=5;
fs=100; % Sampling Frequency
t = n/fs; % time index
% INPUT to Modulator
A = 1 + 0.5*cos(2*pi*1*t);
% OUTPUT
x = A .* sin(2*pi*fc*t);
% FIGURE
figure(1);
subplot(2,1,1);
plot(A);
subplot(2,1,2);
plot(x);

## Slide 4: LAB2: AM Demodulation
Use LAB1 result x and calculate y as each x is squared.
If you connect each peak of y, you can recover original A.

## Slide 5: LAB2： AM Demod answer
n=0:1000; % 1001 points
fc=5;
fs=100; % Sampling Frequency
t = n/fs; % time index
% INPUT to Modulator
A = 1 + 0.5*cos(2*pi*1*t);
% OUTPUT
x = A .* sin(2*pi*fc*t);
%%
y = x .* x;
% FIGURE
figure(2);
subplot(3,1,1);
plot(A);
subplot(3,1,2);
plot(x);
subplot(3,1,3);
plot(y);

## Slide 6: LAB3： Spectrum of square wave
Analyze below pulse spectrum by Discrete Fourier Transform.
0
1
0
1
0
1
0
1

## Slide 7: LAB3： Spectrum answer
n=1:1:80;
x = [zeros(1,10), ones(1,10), zeros(1,10), ones(1,10), zeros(1,10), ones(1,10), zeros(1,10), ones(1,10)];
figure(3)
subplot(2,1,1);
plot(x);
axis([1,80,-0.5, 1.5]);
%%
y = fft(x);
subplot(2,1,2);
plot(abs(y));
axis([1,80,-10, 50]);
Assume T = 10 points

## Slide 8: LAB4： BPSK waveform
Make BPSK waveform as follows
When data=0
When data=1

## Slide 9: LAB4： BPSK answer
n=0:32;
fc=2;
fs=32; % Sampling Frequency
t = n/fs; % time index
% BPSK waveform
x0 = cos(2*pi*fc*t);
x1 = cos(2*pi*fc*t + pi);
% FIGURE
figure(5);
subplot(2,1,1);
plot(x0);
subplot(2,1,2);
plot(x1);
0
(A0, θ0) =(1, 0)
(A1, θ1) =(1, π)

## Slide 10: LAB5： QPSK waveform
Make QPSK waveform as follows
0
(A0, Φ 0) =(1, 1π/4)
(A1, Φ 1) =(1, 3π/4)
(A2, Φ 2) =(1, 5π/4)
(A2, Φ 2) =(1, 7π/4)

## Slide 11: LAB5： QPSK answer
n=0:32;
fc=2;
fs=32; % Sampling Frequency
t = n/fs; % time index
% QPSK waveform
x0 = cos(2*pi*fc*t + 1*pi/4);
x1 = cos(2*pi*fc*t + 3*pi/4);
x2 = cos(2*pi*fc*t + 5*pi/4);
x3 = cos(2*pi*fc*t + 7*pi/4);
% FIGURE
figure(5);
subplot(4,1,1);
plot(x0);
subplot(4,1,2);
plot(x1);
subplot(4,1,3);
plot(x2);
subplot(4,1,4);
plot(x3);

## Slide 12: LECTURE: Complex Exponential Function

## Slide 13: 1. Complex Exponential Function
Real and Imaginary =complex number
Real part is same as previous cosine wave.
Real part
Imaginary part
We will shift from SIN and COS to Complex Exponential Function.

## Slide 14: 2. Real – Imaginary plane
IQ plane
  I: In-Phase = Real axis
  Q: Quadrature-Phase = Imaginary axis
Real-Imaginary plane (Complex plane)
  Complex number can be indicated as a point
Complex plane
0
Real axis (I)
Imaginary axis (Q)
a
b
a + j b

## Slide 15: Complex Exponential Function Shows Rotation in I-Q plane
Real part
Imaginary
0
Real (I)
Imaginary (Q)
A

## Slide 16: Complex Exponential Function shows Rotation on TIME!

## Slide 17: Complex Amplitude (Phaser)
X=x(t=0) shows starting point (t=0) .
X is called as Complex Amplitude (Phaser)

## Slide 18: QPSK by Complex Exponential Function
0
Real (I)
Imaginary (Q)
Complex Amplitude (Phaser) = Constellation point

## Slide 19: Conversion from Complex Exponential Function to Real sinusoid.
Take Real Part
Then
You can convert!

## Slide 20: LAB6： QPSK waveform
Make QPSK waveform as follows using
0
(A0, Φ 0) =(1, 1π/4)
(A1, Φ 1) =(1, 3π/4)
(A2, Φ 2) =(1, 5π/4)
(A2, Φ 2) =(1, 7π/4)

## Slide 21: LAB6： QPSK (2) answer
n=0:32; fc=2;
fs=32; % Sampling Frequency
t = n/fs; % time index
% QPSK Phasers
X0 = exp(1j*1*pi/4); X1 = exp(1j*3*pi/4);
X2 = exp(1j*5*pi/4); X3 = exp(1j*7*pi/4);
% FIGURE
figure(61); plot([X0, X1, X2, X3], '+');
axis([-1 1 -1 1]);
%
X0wave = X0 * exp(1j*2*pi*fc*t); X1wave = X1 * exp(1j*2*pi*fc*t);
X2wave = X2 * exp(1j*2*pi*fc*t); X3wave = X3 * exp(1j*2*pi*fc*t);
%
figure(62);
XX=real(X0wave); YY=imag(X0wave); ZZ=t;
plot3(XX, YY, ZZ); xlabel ('I'); ylabel('Q'); zlabel('time');
%
figure(63);
subplot(4,1,1); plot(real(X0wave));
subplot(4,1,2); plot(real(X1wave));
subplot(4,1,3); plot(real(X2wave));
subplot(4,1,4); plot(real(X3wave));

## Slide 22: LAB7： Draw BER graph
Make following graph by MATLAB

## Slide 23: LAB7： BER graph answer
EBN0dB = 0:1:20; % EbN0 in dB
EBN0 = 10 .^(EBN0dB/10);
BER_QPSK = 0.5*erfc(sqrt(EBN0));
figure(7);
semilogy(EBN0dB, BER_QPSK);
axis([0 20 1E-6 1]);
xlabel(' Eb/N0 (dB) ');
ylabel(' BER of OPSK');
grid on;
title(' QPSK BER');

## Slide 24: LECTURE: Channel Modeling

## Slide 25: Multipath Channel
Direct path and Delayed paths

## Slide 26: Channel Modeling by Impulse Response
H(z)
Sending Signal
Receiving
Signal
If sending signal is Impulse
then, Received signal has many delayed components.
This outputs shows
CHANEL IMPULSE RESPONSE

## Slide 27: Convolution operation
Channel Impulse Response=(1, 0.5, 0.2)
Send (1, 1, 1, 1, 1) signal
Then Received Signal is (1,1.5,1.7,1.7,1.7,0.7,0.2)
If you multiply two polynomial

## Slide 28: Channel Modeling by Impulse Response
H(z)
Sending Signal
Receiving
Signal
(1, 1, 1, 1, 1)
H(z) =(1, 0.5, 0.2)
(1,1.5,1.7,1.7,1.7,0.7,0.2)
This can be calculated by CONVOLUTION.

## Slide 29: LAB8： CHANNEL
Assume Channel Impulse Response = (1, 0.5, 0.2)
Show each received signal for
  x1 = [1,0,0,0,0,0,0];
  x2 = [1,1,1,1,1,0,0];
  n = 1:100; x3 = cos(2*pi*n/32);

## Slide 30: LAB8： CHANNEL answer
%% CHANNEL
h = [1, 0.5, 0.2];
%% INPUT signal 1
x1 = [1,0,0,0,0,0,0];
y1 =conv(h, x1); % OUTPUT signal
figure(81)% FIGURE
xa=1:7;
subplot(2,1,1); stem(xa, x1(1:7)); title('TX');
subplot(2,1,2); stem(xa, y1(1:7)); title('RX');
%% INPUT signal 2
x2 = [1,1,1,1,1,0,0];
y2 =conv(h, x2); % OUTPUT signal
figure(82)% FIGURE
xa=1:7;
subplot(2,1,1); stem(xa, x2(1:7)); title('TX');
subplot(2,1,2); stem(xa, y2(1:7)); title('RX');
%% INPUT signal 3
n = 1:100; x3 = cos(2*pi*n/32);
y3 =conv(h, x3);% OUTPUT signal
figure(83)% FIGURE
xa=1:100;
subplot(2,1,1); stem(xa, x3(1:100)); title('TX');
subplot(2,1,2); stem(xa, y3(1:100)); title('RX');

## Slide 31: LECTURE: OFDM Modeling

## Slide 32
OFDM digital communication WORK SHEET
We are going to send 8bits by the following OFDM communication system
00011011
①
00
01
10
②
M A P
11
I
Q
00
01
10
11
d0=1+j
d1=-1+j
d2=1-j
d3=-1-j
③
I
F
F
T
u0
u1
u2
u3
④
G I add
u0
u1
u2
u3
u3
OFDM
GI
u0
u1
u2
u3
u3
⑤
G I rmv
u0
u1
u2
u3
⑥
F
F
T
d0=1+j
d1=-1+j
d2=1-j
d3=-1-j
⑦
De M A P
00
01
10
11
⑧
00011011
u3
u0
u1
u2
u3

## Slide 33: LAB9 OFDM
Please draw OFDM symbol complex wave form including GI when you send “00011011”.
Please draw OFDM symbol complex wave form including GI when you send “10010011”.
Please draw OFDM symbol complex wave form including GI when you send “00000000”.
Compare those 3 waveform. Then Did you find any problem? If yes, please state the problem.
Time
Time
I
Q
Effective Symbol
GI

## Slide 34: LAB9 1) answer
%%
data=[0,1,2,3]; % 0->00, 1->01, 2->10, 3->11
% MAP
modqpsk= [1+i, -1+i, 1-i, -1-i];
const =modqpsk(data+1);
% IFFT
uu = ifft(const);
% GI ADD
uu_g =[uu(4), uu];
% FIGURE
figure(81)
subplot(3,1,1); plot(real(uu_g),'*-'); axis([1 5 -2 2]);
subplot(3,1,2); plot(imag(uu_g),'*-'); axis([1 5 -2 2]);
subplot(3,1,3); plot(abs(uu_g),'*-'); axis([1 5 -2 2]);

## Slide 35: LAB10 OFDM
MAKE 100 symbol OFDM signal based on previous 4 point OFDM + 1 point GI.
Add noise of SNR=10dB

## Slide 36: LAB10 OFDM answer
% Simple OFDM system (send 8 bits/symbol * 100 symbol)
% Fire Wada
clear all;
num_symbol = 100; % number of symbols
n_symbol = 4; % points in symbol
M = 4; % size of signal constellation
modqpsk= [1+i, -1+i, 1-i, -1-i];
%% 1 . create random data
data = floor(rand(n_symbol,num_symbol)*M);
%% 2. mapping into I-Q constellation
data_1 = modqpsk(1+data);
figure(100);
subplot(2,2,1);
plot(data_1,'r.');
axis([-3 3 -3 3])
title('data constellation')
data_2 = data_1;
%% 3. IFFT
data_3 = ifft(data_2);
subplot(2,2,2);
plot((real(data_3)),'-');
title('IFFT');
%% 4. GI add
data_4 = [data_3(n_symbol,:);data_3];
%%4.1 Add Noise
sigpower=mean(mean(abs(data_4).^2));
sn= 10; %% 10dB
awgn = (randn(n_symbol+1,num_symbol)+i*randn(n_symbol+1,num_symbol));
awgnpower=mean(mean(abs(awgn).^2));
awgn = awgn/sqrt(awgnpower)*10^(-sn/20)*sqrt(sigpower);
data_4=data_4+awgn;
subplot(2,2,3);
plot(real(data_4),'-');
title('GI add');
%% 5. GI remove
data_5 = data_4(2:n_symbol+1,:);
%% 6. FFT
data_6 = fft(data_5);
subplot(2,2,4);
plot(data_6,'b.');
axis([-3 3 -3 3])
title('receive data constellation')
figure(200)
plot(real(reshape(data_4,(n_symbol+1)*num_symbol,1)));

## Slide 37: LAB10 OFDM answer

## Slide 38: LAB11 Symbol Error Rate
Measure Symbol Error Rate for LAB10.
Add noise of SNR=0dB, 5dB, 10dB.
Use ‘demapQPSK.m’ function.
Put the m-file in same directory.
% demapQPSK.m
% The program demap to Complex to Numerical data.
function graycode = demapQPSK(comp)
re = real(comp);
im = imag(comp);
if (re >= 0 & im >= 0 ) graycode=0;
elseif (re < 0 & im >= 0 ) graycode=1;
elseif (re >= 0 & im < 0 ) graycode=2;
else graycode=3;
end

## Slide 39: LAB11 Symbol Error Rate
% Simple OFDM system (send 8 bits/symbol * 100 symbol)
% Fire Wada
clear all;
num_symbol = 100; % number of symbols
n_symbol = 4; % points in symbol
M = 4; % size of signal constellation
modqpsk= [1+i, -1+i, 1-i, -1-i];
%% 1 . create random data
data = floor(rand(n_symbol,num_symbol)*M);
%% 2. mapping into I-Q constellation
data_1 = modqpsk(1+data);
data_2 = data_1;
%% 3. IFFT
data_3 = ifft(data_2);
%% 4. GI add
data_4 = [data_3(n_symbol,:);data_3];
%%4.1 Add Noise
sigpower=mean(mean(abs(data_4).^2));
sn= 5; %% 10dB
awgn = (randn(n_symbol+1,num_symbol)+i*randn(n_symbol+1,num_symbol));
awgnpower=mean(mean(abs(awgn).^2));
awgn = awgn/sqrt(awgnpower)*10^(-sn/20)*sqrt(sigpower);
data_4=data_4+awgn;
%% 5. GI remove
data_5 = data_4(2:n_symbol+1,:);
%% 6. FFT
data_6 = fft(data_5);
figure(11)
plot(data_6,'b.');
axis([-3 3 -3 3])
title('receive data constellation')
%% 7. recover data
rdata=zeros(n_symbol,num_symbol);
for sym = 1: num_symbol
for index = 1:n_symbol
rdata(index, sym) = demapQPSK(data_6(index,sym));
end
end
%% 8. measure Symbol Error Rate by compare data and rdata
Total_data= n_symbol*num_symbol;
diff = rdata - data;
% count how many not zero in diff
notZero = (diff ~= 0);
Total_error=sum(sum(notZero));
fprintf('*** SNR =%4.2f, *** SYMBOL ERROR RATE = %8.5f *** \n', sn, Total_error/Total_data);

## Slide 40: TASK1
Make a Matlab program to measure Symbol Error Rate vs SN ratio in 1K OFDM with QPSK modulation
  FFT size = 1024 points in 1 symbol
  GI length = 1/8*FFT size = 128 points
  Total 100 symbol
Write Mid Report to explain OFDM simulation including
Your Matlab program
Total 100 symbol waveform
Consternation with SNR=0, 3, 6, 9dB
Symbol Error Rate vs SNR Graph
  Vertical: SER in log scale
  Horizontal: SN ratio 0dB, 1dB … to 10dB